## Slide 1: LLM MoE Multicast Discussions
Jeffrey Zhang, HPE
LLM MoE Multicast Side Meeting, IETF123

## Slide 2: Summary
Good to see the discussion of using multicast
This does not seem to be LLM MoE specific, though
PIM/RIFT-Bidir and BIER may work well
  With assistance from the applications

## Slide 3: Multicast Applicability
Any large-scale, high-rate content replication benefits from multicast
  Not just LLM MoE
  But the benefits need to outweigh the cost of establishing/maintaining multicast states
In the case of LLM MoE (or any AIDC scenario, or any scenario)
  How large are the receiver sets, and how high is the data rate?
    The following slides assume that the set size and/or data rate warrant the use of multicast
  How dynamic/scattered are the receiver sets, and how long do they last?
    The applications can help in this regard

## Slide 4: BIER
BIER does not maintain per-tree state, so it is perfect for scenarios where the receiver sets that may change dynamically or come/go very fast
BIER may not work well if a receiver set is scattered across a large number of nodes
  E.g., receivers scattered across thousands of leaf nodes – many copies of data may need to be sent even if the total number is less than the BitStringLength
If the application can choose the receivers from a set of nodes in the same BIER set, then only one copy is needed

## Slide 5: PIM/RIFT-Bidir
PIM-Bidir is generally considered much simpler and more scalable than PIM-SM
RIFT multicast is similar to PIM-Bidir
  With the enhancement of group-prefix-based trees
Both require the pre-establishment of trees
The application may be smart enough to pre-establish enough trees, each with a pre-determined set of receivers, and dynamically choose which tree to use for a particular flow
  E.g. tree1 for expert(1,2), tree2 for expert(3,4), tree3 for expert(5,6), …

## Slide 6: Summary
Multicast is desired if the benefits outweigh the costs
  In LLM MoE or in general
Applications can help reduce the impact of the following
  Scattered receivers – BIER would work well
  Burstiness of flows – PIM/RIFT-Bidir would work well (if BIER is not feasible)